## Slide 1
Simulation and Modeling of Dynamic Systems with Time Varying Device Characteristics
Mansun Chan, Dept. of ECE, HKUST

## Slide 2
What are we modeling?
Passive elements
Sources
Transistors
Transmission lines
Transformers
…
M1 1 0 L=1u W=1u
…
.MODEL XMEM (LEVEL=54 VTO=-0.8V KP=16U
… )
SPICE input deck
Instant parameters for geometry
Model parameters for physical behavior
Model template defined by SPICE

## Slide 3
Device behavior
Device equations
Parameter set
VT=0.7, Cox=xxx, W=xxx, L=xxx
constant currents
t
I
constant
V1(t)
V2(t)
V3(t)
V4(t)
Constant node voltages
t
V(t)
constant
steady state
charging
After reaching steady state
Quasi-Static approximation used

## Slide 4
What are we missing?
Some device are time varying even with constant node voltages such as memory and oscillators
Some systems may drift with time, such as circuit reliability and aging simulation
Self-evolving system such as neuromorphic computing
Device characteristics
t
I
conventional
dynamic
Constant node voltages
t
V(t)
constant
After reaching steady state

## Slide 5
Many memory modeling papers published

## Slide 6
No standard memory model in SPICE yet
No standard models in Commercial SPICE or plans from the Compact Model Coalitions
No agreed framework for memory modeling

## Slide 7
Example: FLASH memory simulation
Equivalent to adding an internal node to keep track of the state variable Vfg(t) and Q(t)
Leading to slower simulation
n+
n+
Indirect method: using the numerical solution in SPICE

## Slide 8
Dynamic System Simulation Methodology
Some instant parameters are used as state variables to calculate the current change
X1 1 0 L=1u W=1u Qg=10p Vt=0.7
…
.MODEL XMEM (VTO=-0.8V KP=16U
… )
instant parameters
model parameters
Need an internal state variable to keep track on the state of the device for each instance
SPICE input deck
More accurate with more internal states without speed penalty

## Slide 9
Example: FLASH memory simulation
Change in internal parameter is more explicitly expressed
n+
n+
Direct method
Direct method
Indirect method
Constant bias
t
V
Accumulated charge
t
Q(t)
Change in VT
t
VT(t)
Change in Current
t
ID(t)

## Slide 10
Example: phase change memory
The state variable is not an electrical but a physical quantity referred to as a crystal fraction
Subcircuit (K. C. Wong et. al. EDSSC 2009)
Need to express the state variable into a time dependent linear differential equation to implement it into a subcircuit
Or the crystal fraction can be treated as an internal parameter that change with time
The Johnson-Mehl-Avrami (JMA) equation

## Slide 11
Defining Initial States
How to define at the initial values of the internal state variables such as crystal fraction?
Users maybe asked to enter the values
  How to extract these parameters from observable measurement results?
Let users input some physically measureable quantity like resistance and the state variables are internally extracted?
  No guarantee it can be achieved
Assume all cells start from one of the states
  A pre-program run is necessary to define the internal state of the cells

## Slide 12
Generic approach to remove internal nodes
Many memory models are based on macro-model approach with many internal nodes
K. Sonoda, Renesas Technology
Example, the temperature model for a PCM cell
The temperature can be represented by an internal parameter
More commonly, it is represented by a voltage obtained from a subcircuit

## Slide 13
Effects of internal nodes
Jacobian Matrix in SPICE
Each internal node creates one entry in the matrix
As these nodes are isolated from other nodes, they directly increase the size of the Jacobian matrix

## Slide 14
Example: a n-stage ring oscillator
With out internal nodes, the size of the Jacobian matrix ~ (n+2)2
With one additional internal node for each transistor, the size of the Jacobian matrix increased to ~ (3n+2)2
Simulation time increase with the size of the Jacobian matrix in the order of O(n1.4) which is about 4.7 times

## Slide 15
Eliminating internal nodes
Jacobian Matrix in SPICE
As the node is loosely coupled, it can be directly evaluated without putting into the Jacobian matrix

## Slide 16
Eliminating internal nodes
Jacobian Matrix in SPICE
As the node is loosely coupled, it can be directly evaluated without putting into the Jacobian matrix

## Slide 17
Simulation flow
The internal node can be eliminated without making any differences
Lining Zhang et. al., JEDS Jan. 2018

## Slide 18
Non-quasi-effects in MOSFETs
The approach is generic and can be used in any isolated internal nodes
Using the direction evaluation for NQS effect in BSIM

## Slide 19
Convergence issues
Some model contain switches causing convergence problem
a generic smoothing hysteresis function can be used
S is a hysteresis function between 0-1 with Vlow and Vhigh as the two triggering point
K. C. Wong et. al. EDSSC 2009
S(V)
V
Vlow
Vhigh

## Slide 20
Simulation Example
Simulation of a PCM cell array without speed and convergence problems
read high
set
reset
read low
read high

## Slide 21
Another type of dynamic system: Device degradation
With a constant bias, the device characteristics still drift with time with rate depends on bias condition
VD
VG
t
VT
t
ID
bias2
bias1
bias1
bias2
Usually modelled as change of some parameters over time
For example: NBTI hole trapping model (P. M. Lenahan, TDMR 11(2), 2011)
Currently, neither modeled by internal parameter or internal node

## Slide 22
Extracting degradation characteristics
Normally, a constant bias is applied because actual waveform is during operation is unknown
VD
VG
t
VT
t
ID
bias2
bias1
bias1
bias2
@ age1
fresh
@ age-n
flesh
age1
age2
age1
age2
flesh
age1
age2
age1
age2
A parameter is used to keep track of the “age” of the device
The time required to reach different age at different bias condition is recorded
A set of parameters extract at different age at a constant bias is used for the aged simulation

## Slide 23
Aging simulation
fresh
age 1
age 2
age-n
Input Deck
fresh model parameter file
SPICE Circuit Simulation
Post-processor and projection
Output
aged model parameter file
Loop
A post-processor is needed to convert the wave form at individual terminal to accumulated degradation
Vn
t
tsim
Vn
t
Dage1
VT
VTaged
Dage2
Data points from table
t

## Slide 24
Industrial application example
It is done by MOSRA in Synopsys or RelXpert in Cadence
Using short term simulation with fresh device data to project long term degradation
https://pdfs.semanticscholar.org/3f78/524f5c3e6d7da1b2f4c322031ad1f415da80.pdf
Vn
tsim
t
taged
No continuous evolution

## Slide 25
Single step aging simulation with dynamic parameters
SPICE
Time accumulation recorded by age
Time dependent parameters VT(age), m(age) from reliability models
The reliability simulation loop is combined with the SPICE circuit simulation loop
More powerful, but faster and simpler simulation flow
Reliability model work closer to the device physics (e.g. impact of self-heating on NBTI become possible)
Drawback: reliability model have to be developed together with the core model instead of a universal add-on
at any age in the life of the circuit
Input Deck
fresh model parameter file
Output

## Slide 26
Including parameter update in aging simulation
versus
The final current is used to project the parameter degradation
Including hot carrier Vth degradation model

## Slide 27
Fitting degradation data
Degradation rate deviates from the general power-law time-function prediction
Static data extraction cannot handle dynamic behavior
t
Vin
NBTI
Using dynamic parameter update does not require to change the underlying physics under static bias

## Slide 28
Runtime example
Aging description
Parameter update
Time evolution of current degradation
flesh
degraded
In addition to the result, the degradation process can be simulated

## Slide 29
From static data to switching behavior
Device level aging parameters are extracted based on static biasing data
How to accumulate “age” from different characteristics when varying inputs are used?
Vbias
t
DVT
t
V3
V2
V1
V3
V2
V1
Vbias
t
?

## Slide 30
Calculating age accumulation
What about switching to different curve at the time when input voltage is changed?
Vbias
t
DVT
t
V3
V2
V1
V3
V2
V1
DVT
t
?
?
Need to find out the current state with respect to the new characteristics before switching
Vbias
t
DVT
t
V3
V2
V1
V3
V2
V1

## Slide 31
Dynamic age accumulation
A equivalent time point teq is used to start the aging condition
Steps:
  Start with teq1=0 for degradation under Vstr1 ending at Δt to calculate DVth(Δt)
  calculate equivalent start time (teq2) of based on DVth(Δt) and characteristics of ΔVth2
  second period start at teq2 to (teq2+Δt) at which ΔVth2(teq2+Δt) is calculated and used to calculate the teq for next period

## Slide 32
Dynamic voltage step
It is possible that at some high biasing point, the device has aged enough that no more aging occurs when switched to a lower voltage
The dynamic age accumulation algorithm keeps the present age without further degradation

## Slide 33
NBTI example
Data from J. Velamala, et al., IRPS 2013, p. CM.3.1.
The dynamic aging accumulation approach is able to handle NBTI degradation with random switching

## Slide 34
Performing long term aging simulation
How to simulate aging over long period of time, say 10 years?
Time Tracing method:
  physically extend the time axis to over 10 years
  Most accurate but very time consuming
Direct projection:
  Using a very short period of simulation and directly project results on the other end of the time axis based on certain projection function
  Need to assume same short-term and long-term mechanisms
  Fast but only very crude projection

## Slide 35
Current approach
Using a short period of simulation and directly project to the required lifetime
Further degradation in intermediate time is ignored
If short-term and intermediate term degradation mechanism is different, the projection may be incorrect
DVT
t
fresh
aged
projection
1s
1s
(10 year)
t
1s
2s
total time in simulation

## Slide 36
Degradation mechanism example
Interface state generation dominate in short term and hole-trapping dominate in intermediate term
J. B. Velamala, IRPS, p. CM.3.1, 2013
P. M. Lenahan, TDMR 11(2) p. 219, 2011
hole-trapping model
Interface state generation

## Slide 37
Adaptive projection method
Divide the aging period into Ncyc uneven cycles
For the ith cycle, it is further divided into of a time tracing period of tcyc and a project period of tcyc*2i
Example
10 year simulation time is mapped to 1.08msec

## Slide 38
Example: device characteristics
It takes about two hours to perform the simulation with time tracing and only 10s with the adaptive projection method with minimal error

## Slide 39
Example: ring oscillator
The module has been implemented into a circuit simulator and it ready for trial

## Slide 40
Other applications
Circuit failure due to electromigration
Use layout extractor to extract the wire resistance
Dynamic parameter change included in the extracted resistance
More holistic simulation tracking the time evolution of the entire circuit instead of just a ”pass/fail” qualification process

## Slide 41
Summary
Compact models are mainly developed for static systems
Dynamic instant parameters play a more important role in dynamic system to record the status of a device
Internal nodes should be eliminated to improve simulation speed and a generic approach has been developed for such purpose
A more systematic approach is needed to model memory devices for neuromorphic computing
A more holistic reliability simulation approach is demonstrated
A few questions remains, for example, how to perform parameter extraction for a dynamic system?

## Slide 42
http://i-mos.org/
More resources

## Slide 43
https://www.edx.org/course/principle-of-semiconductor-devices-part-i-semiconductors-pn-junctions-and-bipolar-junction-transistors-1
An animation based semiconductor class:
Part I: PN Junction and BJT
An advertizement
Part II: FETs and MOSFETs
https://www.edx.org/course/principle-of-semiconductor-devices-part-ii-field-effect-transistors-and-mosfets